Slide 1

Read the following italic to the students

- INTRODUCTION

  - Welcome students

    - Class rules

  - Instructor name

- COURSE TITLE

  - Land Navigation with Lensatic Compass

- LESSON TOPIC NUMBER

  - Part 1 Basics  Land Navigation

- STUDENT OBJECTIVE  The student will  be able to  . .

  - Understand the basic use of a lensatic compass.

  - Read and interpret a map.

  - Perform basic navigation with a map and lensatic compass.

- COURSE OBJECTIVE

  - How to select a quality lensatic compass.

  - How to identify lensatic compass features and its use.

  - How to read and sight a lensatic compass.

  - How to read and interpret map symbols and information.

  - How to orient a map with land features.

  - How to convert azimuths between map and compass.

- TESTING

  - Written exam (To show yourself what you have learned)

  - Orient a map (Show that you can do it)

  - Sighting a compass (Show that you can do it)

- TIME - 8 hrs / 10 min breaks per hour /  ½ hr lunch

- INSTRUCTIONAL AIDS

  - PowerPoint Presentation & Projector

  - Lensatic Compasses

    - Genuine for students to use (as many as needed)

    - Fake to compare (quantity 3 different  types)

  - Common Compass (for slide 33)

  - Maps (as many as needed)

    - Preferably of the local area

    - Sample of a protected map (see slide 89)

    - Sample of dirty worn map (see slide 89)

    - Sample of properly folded map ( slide 90)

  - Protractors (as many as needed)

  - Student handbooks

  - Mil-Prf-10436N Lensatic Compass Specifications

  - Exams & pencils

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

  - _________________________________

Slide 2

Read the following italic to the students

“Using the military lensatic compass we will learn basic land navigation skills to keep us from getting lost.”

Slide 3

Read the following italic to the students

“This is why you are here, to learn from a knowledgeable and skilled Instructor.”

- SUMMARIZE INSTRUCTOR’S SKILLS

  - 30 seconds to 1 minute long

  - Instructor’s experiences.

    - Using the lensatic compass

    - Land Navigation skills

Slide 4

Read the following italic to the students

“Many of the examples presented in this course, we will put to practice, for clarity.”

Slide 5

Read the following italic to the students

“Any questions?”

- HANDOUT MATERIALS

  - Student Handbooks

  - Statement of Liability form

  - Compasses

    - Have students inspect the compass

    - Have students annotate on the Liability form any damages found on the compass

  - Maps

  - Pencils

  - Other course materials

- ENSURE STUDENTS HAVE

  - Required equipment before continuing

  - Or pair up students to share equipment

Slide 6

Read the following italic to the students

“Again, before we continue, are there any questions?”

Slide 7

Read the following italic to the students

Slide 8

Read the following italic to the students

- Tracking present location (Where am I?)

“You definitely need to know where you are, to know what direction to go.”

- Determining Distance (How far is it and am I there yet?)

“Knowing distance, you can estimate how much time it will take to get there.”

- Sense of direction (Where do I want to go and where am I actually going?)

“You heard that saying, follow your nose.  While, you cannot follow your nose if your nose does not know what direction to go.”

“And sometimes you have to go in one direction to get to another place in a different direction.  (getting around obstacles; a hill, dense jungle, or swamp) “

- How to read a topographic map (Do I understand the map?)

“You cannot make sound decisions where to go, if you cannot understand the map.”

“Just knowing these four basic skills (IN RED) can prevent you from getting lost.”

Slide 9

Read the following italic to the students

- AT THE END OF THE SLIDE

“Again, we will be covering PART 1 BASIC LAND NAVIGATION”

Slide 10

Read the following italic to the students

Slide 11

Read the following italic to the students

- THE LENSATIC COMPASS

  - Description

  - Parts and Features

“What is a lensatic compass and how to identify a genuine one?”

- THE TOPOGRAPHIC MAP

  - Description

  - How to Read

“What are topographic maps and what information are on them.”

- THE LAND

  - Terrain Features

  - Terrain and Map Association

“What is a terrain feature and how to identify them on a map.”

Slide 12

Read the following italic to the students

Slide 13

Read the following italic to the students

- BATTLE TESTED - SHOCK, WATER . .

“Fake lensatic compasses cannot hold up to these environments.”

- LUMINOUS LIGHTS FOR NIGHT NAVIGATION . . .

“Night navigation is taught in PART 4 Expert Land Navigation.”

- COPPER INDUCTION DAMPENING SYSTEM . . .

“There are no liquid fluids in the compass dial, therefore it cannot leak and malfunction like other liquid filled orienteering compasses.”

- A ‘DEEP-WELL’ DESIGN IS USED TO ALLOW . . .

“The world is divided into 5 magnetic zones, going from North to South.  And compasses are designed to only work in a specific zone.

An orienteering compass designed for the northern hemisphere or a specific zone will ‘stick’ in the southern hemisphere, as it will basically be trying to point towards the ground.

However, a GENUINE deep welled Lensatic Compass is designed to be used anywhere in the world.”

Slide 14

Read the following italic to the students

- Pass around the 3 different styles fake lensatic compasses so the students can see and compare the fake to the GENUINE lensatic compass.

- And discusses the faults of the fake lensatic compasses.

  - Liquid filled

  - No fixed index line

  - Different names used for a fake lensatic compass

    - Marching Lensatic Compass

    - Military Style Compass

    - Engineering Lensatic Compass

    - And many more

Slide 15

Read the following italic to the students

Slide 16

Read the following italic to the students

- BEFORE CONTINUING WITH SLIDE

“The lensatic compass has 3 PARTS with features on each part.”

“As we go through these PARTS and FEATURES, we will go into more detail on each feature on the next slides.  Right now we are just going to go through the names of each item.”

- CONTINUE WITH THE SLIDE

PARTS

    - Cover

    - Base

    - Lens Rear Site

FEATURES

    - Luminous Sighting Dots

    - Sighting Wire

    - Etc

Slide 17

Read the following italic to the students

- SIGHTING WIRE

“If the wire was to fall off, you still can use the sighting window.”

- LUMINOUS SIGHTNG DOTS

“More details are explained in PART 4 Expert Land Navigation.”

Slide 18

Read the following italic to the students

- BEFORE CONTINUING WITH SLIDE

BASE – The Main body of the compass.  If for any reason . . .

“The lensatic compass is so durable that it will never malfunction, unless you deliberately mistreat, or break the lensatic compass.”

- CONTINUE WITH THE SLIDE

Thumb Loop – to hold compass with the thumb.

“Details how to use the thumb loop will be explained later.”

Lanyard Ring – for string or rope.

“Always carry the compass around your neck or an attachment close to your chest, or a chest pocket for easy, quick access.”

Slide 19

Read the following italic to the students

AT THE END OF THE BLACK RING DESCRIPTION

Have students look at the compass.

Slide 20

Read the following italic to the students

AT THE END OF THE RED RING DESCRIPTION

Have students look at the compass.

Slide 21

Read the following italic to the students

Slide 22

Read the following italic to the students

“A good idea is to get two different colored permanent markers or paint and use one to mark every other 5th tick mark for Centimeters and the other for every other 13th tick mark for Inches.

Write on the compass which color represents which measurement, Centimeters or Inches.

Starting from the Zero tick mark when counting and use bright colors that are easy to see.

This will aid you in quicker and more accurate distance measurements on the map.”

MAP SCALE      1 tick mark              1cm	         1 inch

1:24,000	           48 m / 51 yds          240 meters      663 yds

1:25,000	          50 m / 53 yds           250 m	         690 yds

1:50,000	          100 m / 107 yds      500 m	      1390 yds

1:100,000        200 m / 214 yds      1 km	       1.6 miles

- Have a lensatic compass marked with two colors to show students.

- Have students practice measuring on a map with the GRADUATED STRAIGHT EDGE bar scale.

Slide 23

Read the following italic to the students

- Lens – used to read the dial.

“The LENS cannot be used to start a fire in an emergency, when the sun is out and bright.  The lens is not designed to strongly focus the sun rays.  The limited focused sun rays do not get hot enough to start a fire.”

“Remember this is a compass, not a fire starter.”

Slide 24

Read the following italic to the students

Slide 25

Read the following italic to the students

- Give an example of effects of metal on a compass.

- Have students try it themselves.

  - Belt buckle

  - Paper clip

  - Jewelry

Slide 26

Read the following italic to the students

Have students perform each step while lecturing the step.

Slide 27

Read the following italic to the students

- Explain what a CALIBRATION POINT is.  Also known as a compass rose.  A site that is surveyed by a surveyor, for Magnetic North, South, East, and West.

- It is up to the Instructor whether to demonstrate a compass calibration or not.  (If a compass rose is available)

Slide 28

Read the following italic to the students

Slide 29

Read the following italic to the students

“We will discuss two techniques to sight a lensatic compass and the proper procedures to do it.”

Slide 30

Read the following italic to the students

- Demonstrate procedures to the class and . . .

- Explain step-by-step.

  - Place your thumb through the thumb loop, and form a steady base with your third and fourth fingers, and extend your index finger along the side of the compass base.

  - Place the hand holding compass into the palm of the other hand.

  - Bring both hands up to the face and position the thumb that is through the thumb loop against the cheekbone.

  - Look through the lens of the eyepiece. If the dial is not in focus, move the eyepiece up or down until the dial is in focus.

  - Align the sighting slot of the eyepiece with the sighting wire in the cover on the point to which the azimuth is being determined.

  - Look through the lens of the eyepiece and read the azimuth

Slide 31

Read the following italic to the students

“Holding the compass to your cheek is very accurate and steady.”

“You sight your target and then read the azimuth.”

Slide 32

Read the following italic to the students

“This is what you see when looking through the lens at the dial.  You see the current azimuth reading on the Black Index Line, both in degrees and mils.”

Slide 33

Read the following italic to the students

“As you can see, you can observe both the target and azimuth reading by simply shifting your eye up or down.”

“It is very accurate, fast, and easy compared to an orienteering compass.”

Show how a common Compass is difficult to sight and read.

Slide 34

Read the following italic to the students

Slide 35

Read the following italic to the students

“Let’s say you want to know what the azimuth heading is to the water tower, so you can calculate your position.”

Click to next slide

Slide 36

Read the following italic to the students

“Using the compass-to-cheek method . . . click slide . . . this is what you get.”

“65° azimuth, 1,150 mils.”

“Use this information to calculate your position on the map.  This is taught in Part 2 Intermediate Land Navigation.”

Slide 37

Read the following italic to the students

“This is worth repeating.  The Compass-to-Cheek method is very accurate.”

“On the next several slides we are going to see several right and wrong ways of performing the Compass-to-Cheek method.”

Slide 38

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate to the students on the technique in the picture before going to the next slide.

NOTE – have students try this

Slide 39

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate on the technique in the picture before going to the next slide.

Slide 40

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate why it is wrong before going to the next slide.

Slide 41

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate on the technique in the picture before going to the next slide.

“The one hand hold can be used.  This frees the other hand to hold the map.”

NOTE – have students try this.

Slide 42

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate on the technique in the picture before going to the next slide.

“This technique also can be used.  It is a modified compass-to-cheek method hold.”

“It is a matter of preference for the user.”

NOTE – have students try this.

Slide 43

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate on the technique in the picture before going to the next slide.

NOTE – This individual is on the ground doing reconnaissance;

- You can see the pen in his hand and

- You can imagine there is a map next to him or a note pad for writing detailed information.

The bottom line is he is using the compass-to-cheek method.

Slide 44

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate why it is wrong before going to the next slide.

“This technique has no stability.”

Slide 45

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate on the technique in the picture before going to the next slide.

Slide 46

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate why it is wrong before going to the next slide.

“This technique has no stability.”

NOTE – have students try this.

Slide 47

Read the following italic to the students

QUESTION - “Is this individual holding the compass correctly?”

Click slide

Elaborate why it is wrong before going to the next slide.

“This technique has no stability.”

Slide 48

Read the following italic to the students

Slide 49

Read the following italic to the students

- Read the procedures first.

- Have the students try this.

- Procedures continued on next slide.

Slide 50

Read the following italic to the students

- Describe each procedure step-by-step first, before students perform this procedure.

- Pick a random azimuth and have the students perform this procedure using the same random azimuth.

- Verify their readings; they all should be the same.

  - Random azimuth selected

  - Luminous Bezel Line reading.

Slide 51

Read the following italic to the students

Slide 52

Read the following italic to the students

Purpose.   Permit a person to visualize an area of the earth's surface; shows what an area looks like without actually being there.

“We will only be covering the USGS Topographic map; which stands for United States Geological Survey.”

Slide 53

Read the following italic to the students

Read this below before continuing with this slide.

- Characteristics of a Map:

  - Designed to show us common information.

  - Location of ground objects.

  - Populated areas.

  - Routes of travel

  - Communication lines.

  - Extent of vegetation cover.

  - Elevation and relief of the earth's surface.

Slide 54

Read the following italic to the students

Slide 55

Read the following italic to the students

Slide 56

Read the following italic to the students

Slide 57

Read the following italic to the students

Slide 58

Read the following italic to the students

Slide 59

Read the following italic to the students

Slide 60

Read the following italic to the students

Slide 61

Read the following italic to the students

Slide 62

Read the following italic to the students

Slide 63

Read the following italic to the students

“On the LARGE SCALE map you can see the freeway, small road, cemeteries, name of the river, and a trail.”

Slide 64

Read the following italic to the students

“On the SMALL SCALE map all you can see is thousands of square miles of countryside, a city, and freeways, but no detail.”

“On the MEDIUM SCALE map you see more detail, the spring well and a road, but not much.”

“On the LARGE SCALE map you see the exact location of the spring well, more roads, dirt roads, trails, and a building.”

Slide 65

Read the following italic to the students

Slide 66

Read the following italic to the students

“These symbols are constantly refined/updated by the USGS office to better relate to the features they represent, improve the appearance or readability of the map, or reduce production cost.”

“Consequently, within the same series, maps may have slightly different symbols for the same feature.”

Slide 67

Read the following italic to the students

“These are just some examples of map symbol landscapes.”

Slide 68

Read the following italic to the students

Land subject to inundation

“These are areas that either flood seasonally or have flash floods.”

Slide 69

Read the following italic to the students

Well or spring

“A well is man-made and a spring is water that gurgles directly out  of the ground from an underwater river or natural water source.”

Slide 70

Read the following italic to the students

Slide 71

Read the following italic to the students

Slide 72

Read the following italic to the students

AT THE END OF THE SLIDE

- Contour Lines.  The most common way of indicating elevation and relief on maps.

  - The spacing lines indicate the nature of the slope.  This has important significance to the wilderness navigator.

  - Evenly spaced and far apart indicate a uniform gentle slope.

  - The closer the contour lines, the steeper the terrain.

  - Closely spaced at the top and widely spaced at the bottom indicate a concave slope.

  - Widely spaced at top and closely at bottom indicates convex slope.

Slide 73

Read the following italic to the students

- Contour Lines.  The most common way of indicating elevation and relief on maps.

  - A line representing an imaginary line on the ground, along which all points are at the same elevation.

Slide 74

Read the following italic to the students

Slide 75

Read the following italic to the students

BEFORE READING SLIDE

- Contour Lines.  The most common way of indicating elevation and relief on maps.

  - In order to show the relationship of land formations to each other, a map shows a sketch with different relief features and its characteristic contour pattern.

  - Known has TERRAIN RELIEF.

Slide 76

Read the following italic to the students

Ridge.  A line of high ground, with normally minor variations along its crest.  The ridge is not simply a line of hills; all points of the ridge crest are higher than the ground on both sides of the ridge.

Slide 77

Read the following italic to the students

Hill.  A point or small area of high ground.

Slide 78

Read the following italic to the students

Saddle.  A dip or low point along the crest of a ridge.  A saddle is not necessarily the lower ground between two hilltops; it may simply be a dip or break along an otherwise level ridge rest.

Slide 79

Read the following italic to the students

VALLEY. A valley is a course of a stream that has at least a limited extent of reasonably level ground bordered on the sides by higher ground.

The valley generally has maneuvering room within its confines. Contours indicating a valley are U-shaped and tend to parallel a major stream before crossing it.

The more gradual the fall of a stream, the farther each contour parallels it. The curve of the contour crossing always points upstream.

Slide 80

Read the following italic to the students

Depression.  A low point or sinkhole, surrounded on all sides by higher ground.

Slide 81

Read the following italic to the students

Spur.  A usually short, continuously sloping line of higher ground normally jutting out of a ridge.

SPURS are also called FINGERS.

Slide 82

Read the following italic to the students

Draw.  A less developed stream course in which there is essentially no level ground and therefore, has little or no maneuver room within its confines.  The ground slopes upward on each side and towards the head of the draw, contours indicating a draw are 'V" shaped, with the point of the "\/" toward the head of the draw.

Slide 83

Read the following italic to the students

Cliff.  A vertical, or near vertical, slope.  When a slope is so steep that it cannot be shown at the contour interval, it is shown by a ticked line carrying contours.  The ticks always point toward lower ground.

Slide 84

Read the following italic to the students

Cuts & Fills.  Man made features by which the bed of a road or railroad is graded or leveled off by cutting through high areas and filling in low areas along the right of way.

Slide 85

Read the following italic to the students

Slide 86

Read the following italic to the students

Slide 87

Read the following italic to the students

Slide 88

Read the following italic to the students

G-M ANGLE . . .

“if GN and MN are on the opposite side of True North, then you ADD GN and MN values to get G-M ANGLE.”

“But, if GN and MN are on the same side of True North, then you SUBTRACT the smaller value from the bigger value to get G-M ANGLE.”

AT THE END OF THE SLIDE “With MN and …”

“We will practice this later in another slide.”

Slide 89

Read the following italic to the students

“Choose the one that is easier for you to remember.”

Slide 90

Read the following italic to the students

Give the following information to the students to practice this.

- From GROUND to MAP

  - You target a landmark at MN azimuth 17º to a hill.

  - What is the map GN azimuth from your location?

    - Answer (353º)

    - 17º – 24º = - 7º  (360º – 7º = 353º)

- From MAP to GROUND

  - With protractor and map, you plot a GN azimuth 112º to a lake

  - What is the ground MN azimuth from your location?

    - Answer (136º)

    - 112º + 24º = 136º

Slide 91

Read the following italic to the students

Give the following information to the students to practice this.

- From GROUND to MAP

  - You target a landmark at MN azimuth 17º to a hill

  - What is the map GN azimuth from your location?

    - Answer (26º)

    - 17º + 9º = 26º

- From MAP to GROUND

  - With protractor and map, you plot a GN azimuth 112º to a lake

  - What is the ground MN azimuth from your location?

    - Answer (103º)

    - 112º - 9º = 103º

Slide 92

Read the following italic to the students

Slide 93

Read the following italic to the students

AT THE END OF THE SLIDE “NOTE if you have…”

“We will practice using a protractor on the next slides.”

NOTE – “More detailed use of the protractor is covered in . . .

Part 2 INTERME

DIATE LAND NAVIGATION.”

Slide 94

Read the following italic to the students

Have Instructor pick a random position on the map and a random destination point on the map and have the students practice this technique.

Have students also practice the Map-to-Compass and Compass-to-Map conversions from SLIDE 73.

Slide 95

Read the following italic to the students

Slide 96

Read the following italic to the students

Slide 97

Read the following italic to the students

Have students practice this.

Slide 98

Read the following italic to the students

This technique is used when the map does not have a MAGNETIC DECLINATION drawn on the map.

Slide 99

Read the following italic to the students

Have students practice this outside.

Slide 100

Read the following italic to the students

Slide 101

Read the following italic to the students

Slide 102

Read the following italic to the students

AT THE END OF THE SLIDE “Example below shows…”

More detail covered in Part 2 INTERMEDATE LAND NAVIGATION.

Slide 103

Read the following italic to the students

AT THE END OF THE SLIDE  “Navigation is not about finding…”

More detail covered in Part 2 INTERMEDATE LAND NAVIGATION.

Slide 104

Read the following italic to the students

Slide 105

Read the following italic to the students

AT THE END OF THE SLIDE “Scan the Landscape…”

“This is where binoculars are very useful; for scanning the landscape.”

“Here you can see the hazard; if you were not careful, you could end up falling into the bottom of the pit.”

Slide 106

Read the following italic to the students

Slide 107

Read the following italic to the students

“Ignore the blue triangles; I couldn’t erase them from the diagrams.”

*  USE A POINTER to point out on the screen.

GREEN CIRCLE – shows the river bend.

RED CIRCLE – shows the open field.

“As you can see;

TOPO MAP show general symbols.

AERIAL PHOTO shows a 3D visual of the land.

LAND shown over time can be different (change) from both maps.”

Slide 108

Read the following italic to the students

“Here is another example.”

Give students more detail of “what-is-what” on the picture and on the map.

*  USE A POINTER to point out on the screen.

- Trees.

- Shrubs on very steep hill.

- Open, swampy field.

- However, on the map you see the trial and river; but on the landscape, you cannot see the trial or the river that flows into the pond.

Slide 109

Read the following italic to the students

“Here is another example.”

NOTE – give students more detail of “what-is-what” on the picture and on the map.

*  USE A POINTER to point out on the screen.

- Small river pond.

- Strip of trees and clearing.

- Island.

- Big clearing.

Slide 110

Read the following italic to the students

“Here you will see the same area at two different vantage points.  Remember, an area in front of you looks different from behind you, after you pass it.”

Slide 111

Read the following italic to the students

Slide 112

Read the following italic to the students

Slide 113

Read the following italic to the students

Slide 114

Read the following italic to the students

“In the middle of the picture, in the foreground of McHenry Notch,  Lake Powell is down below, in the valley.”

Slide 115

Read the following italic to the students

“Remember, an area in front of you looks different from behind you, after you pass it.”

Slide 116

Read the following italic to the students

Slide 117

Read the following italic to the students

- Have samples of folded maps. (SEE NEXT PAGE/SLIDE)

- Have a sample of a map not taken care of; all full of dirt and worn.

Slide 118

Read the following italic to the students

- Have students practice this.

- Have samples.

Slide 119

Read the following italic to the students

Slide 120

Read the following italic to the students

Slide 121

Read the following italic to the students

- Give written exam.

  - Review questions and student answers.

  - Grade exams.

- Give hands on exam – SIGHT A COMPASS.

  - Observe student’s techniques.

  - Assist students as needed.

- Give outdoors exam – ORIENT A MAP.

  - Observe student’s techniques.

  - Assist students as needed.

Slide 122

Read the following italic to the students